## Slide 2: DCS
17.4.25

## Slide 3: Distributed Control Systems
DCS is also a collection of components used for the same purpose like SCADA.
SCADA * DCS,……
Are they essentially the same????....

## Slide 4: DCS & SCADA ?
DCS’s role in plant automation is the same as the SCADA system.
Thus the role of SCADA and DCS systems are essentially the same,….

## Slide 5: DCS, SCADA…
DCS and PLC systems both are actually factory centered systems whereas your SCADA can be geographically dispersed.
DCS are for factory environment,
For instance, site ( A ) in a country, site (B) in another country and site (C) in another and communicate with each other, DCS system will never ever apply there. definitely shall rely on the SCADA system.

## Slide 6: DCS & SCADA
DCS, a factory centered hence there is a short distance communication in DCS system comparative to SCADA system, hence DCS has high speed communication
DCS systems……….. are redundant…. that means each area have instead of one employ two controllers.
Each unit would be actually managed and controlled by a separate system of two controllers.

## Slide 7: DCS & SCADA
DCS system main job is to control the process and it relies on instrumentation sensors and controllers whereas your…….SCADA is not so,, it is event driven,…..

## Slide 8: COMPUTERS IN AUTOMATION
The integration of computers into automation has revolutionized industries, enhancing efficiency, precision, and productivity……
Automation refers to the use of technology to perform tasks with minimal human intervention, and computers play a crucial role in controlling and managing automated systems.

## Slide 9: INTRODUCTION OF COMPUTERS IN AUTOMATION
1. Large and Bulky :
Early computers, such as the ENIAC (1946) and UNIVAC (1951), occupied entire rooms and required extensive cooling and maintenance.
2. Limited Processing Power
These machines had very low computational speed and storage capacity.

## Slide 10: INTRODUCTION OF COMPUTERS IN AUTOMATION
3. Basic Control and Automation
Early industrial automation relied on relay-based control systems, which were later replaced by Programmable Logic Controllers (PLCs) in the 1960s.
4. Lack of Real-time Processing
Early computers could not process real-time data efficiently

## Slide 11: INTRODUCTION OF COMPUTERS IN AUTOMATION
5. High Cost and Limited Availability
Only large corporations only could afford computers.
The cost of hardware and maintenance was extremely high, limiting its widespread adoption.

## Slide 12: Computers in the field of control in Industries
DATA LOGGING USING A COMPUTER
All loops are analog control loops (With Analog Controller) with manual SP given by the operator.
Every loop had 3 elements, M, C and FCE.
2. SUPERVISORY CONTROL USING COMPUTER
Computers were used to provide the SP, however the loops were still analog loops (With Analog Controller)
Computer to monitor the process and just to give any change in SP.
Every loop hence had M, C and FCE.( with SP given by the computer)

## Slide 13: Computers in the field of control in Industries
DIRECT DIGITAL CONTROL
Computers are used as Controllers, it eliminated the need of an analog controller.
Hence the loops had only a measuring device and a FCE.

## Slide 14
CENTRAL COMPUTER SYSTEM ARCHITECTURE
All system functions are implemented in high-performance computer hardware in a central location.
In general, redundant computers are required so that the failure of a single computer does not shut the whole process down.

## Slide 15: DCS( Distributed Control System)- Intro
Objectives in the development of DCS is to maintain the best features of the central computer control and hybrid architectures.
It combines the power and flexibility of digital control with the user-oriented familiarity of the traditional analog and sequential control system.

## Slide 16: DCS Benefits
DCS provide the following benefits:
Complex structures: Unlike comparable programmable logic controllers (PLCs), a DCS can access large amounts of information in a complex environment.
System redundancy: If a processor fails, the redundancy provided in the DCS ensures that only one section of the plant's processes is interrupted.
Scalability : More control or process units can be added whenever needed. Adding more I/O modules to a controller also extends I/Os.
Security : ecurity and cybersecurity capabilities are enabled at the engineer and operator levels.

## Slide 17
DISTRIBUTED CONTROL SYSTEMS - ARCHITECTURE
V

## Slide 18
A generalized DCS architecture consists of:
LOCAL CONTROL UNIT (LCU)
LOW-LEVEL HUMAN INTERFACE (LLHI)
DATA INPUT/ OUTPUT UNIT (DI/OU)
HIGH LEVEL HUMAN INTERFACE (HLHI)
HIGH-LEVEL COMPUTING DEVICE (HLCD)
COMPUTER INTERFACE DEVICE (CID)
SHARED COMMUNICATION FACILITIES
DISTRIBUTED CONTROL SYSTEMS - ARCHITECTURE

## Slide 19
DISTRIBUTED CONTROL SYSTEMS - ARCHITECTURE
A generalized DCS architecture consists of:
LOCAL CONTROL UNIT (LCU) – The smallest collection of hardware in the system that can do closed loop control. The LCU directly interfaces to the process
Why named as LCU..
Local controller, not that to understand as ..they act locally, …………………………………..
they are situated in the plant(floor) and taking care of the loop in which it is employed and (which must be) of rugged in nature….

## Slide 20
DISTRIBUTED CONTROL SYSTEMS - ARCHITECTURE
A generalized DCS architecture consists of:
LOCAL CONTROL UNIT (LCU) – The smallest collection of hardware in the system that can do closed loop control. The LCU directly interfaces to the process
LOW-LEVEL HUMAN INTERFACE (LLHI) – A device that allows the operator or instrument engineer to interact with the LCU. [to change SPs, control modes, control configurations or tuning parameters]. LLHI can also interface directly to the process. Operator-oriented hardware at this level is LL operator interface. (LL engineering interface)

## Slide 21
DATA INPUT/ OUTPUT UNIT (DI/OU) – A device that interfaces to the process for the purpose of acquiring and outputting data. It performs no control functions
HIGH LEVEL HUMAN INTERFACE (HLHI) - A collection of hardware that performs functions similar to the LLHI but with increased capability and user friendliness.
It interfaces to other devices via shared communication facilities. Operator-oriented hardware at this level is HL operator interface.
HIGH-LEVEL COMPUTING DEVICE (HLCD) A collection of microprocessor based hardware that performs plant management functions traditionally performed by a plant computer.
It interfaces to other devices only over the shared communication facilities.

## Slide 22
COMPUTER INTERFACE DEVICE (CID) A collection of hardware that allows an external general-purpose computer to interact with other devices in the DCS (distributed control system) using the shared communication facilities.
SHARED COMMUNICATION FACILITIES One or more levels of communication hardware and associated software that allow the sharing of data among all devices in the distributed system.
DISTRIBUTED CONTROL SYSTEMS - ARCHITECTURE

## Slide 23
DISTRIBUTED CONTROL SYSTEMS - ARCHITECTURE

## Slide 24
THANK YOU…….

## Slide 25: CIA 2
TOPICS:
  SS modeling of Mechanical systems
  Controllability, Observability
  State feedback controller
  State Observer
  UNIT 4
  DCS architecture..
  PLC program…(LATCH, interlocking concept)

## Slide 26: CIA 2
ADDITIONAL TOPICS:
  SCADA
  DAQ
  PID controller

## Slide 27: CIA 2
PATTERN:
PART A ( 40 MRKS)
To answer any four / five questions….
PART B ( compulsory question)(10 Mrks)
1 question ( with subdivisions, covering the full syllabus..)
  (NO CHOICE in this PART..)
  ***********

## Slide 28
THANK YOU…….